1.
What appears to be a character on the keyboard or screen is of course, like everything else,
stored internally just as a bit pattern. The type char is specifically meant for storing such
character data, but any integer type can be used. We used int for a subtle but important
reason.
The problem is distinguishing the end of input from valid data. The solution is that getchar
returns a distinctive value when there is no more input, a value that cannot be confused with
any real character. This value is called EOF, for ``end of file''. We must declare c to be a type
big enough to hold any value that getchar returns. We can't use char since c must be big
enough to hold EOF in addition to any possible char. Therefore we use int.

2.
The parentheses around the assignment, within the condition are necessary. The precedence
of != is higher than that of =, which means that in the absence of parentheses the relational
test != would be done before the assignment =. So the statement
c = getchar() != EOF
is equivalent to
c = (getchar() != EOF)

3.
long integers are at least 32 bits. Although on some machines, int and long are the same
size, on others an int is 16 bits, with a maximum value of 32767, and it would take relatively
little input to overflow an int counter. The conversion specification %ld tells printf that the
corresponding argument is a long integer.